Two-speed OF
By :
Aditi Pradeep
University of British Columbia

---
Hybrid readout scheme
Phonon trace
Charge trace

---
Correlation in hybrid readout
n	1	2	...	32...	...64...	...96...	..128..	...	1024
(Hz)	19.1	38.2	...	610.4	1220.7	1831.1	2441.4	...	19531.25
f_{slow}
n	1	2	3	4	...32...	...512
(Hz)	610.4	1220.7	1831.1	2441.4	19531.25	312500
f_{ fast }
Downsampling results in loss of information beyond f_(slow) > 19.531KHz for the slow region, resulting in those frequencies getting aliased into f_(slow)<f_(Nyq).

---
Correlation in hybrid readout
2. In the optimal filtering process, this is reflected by a change in the covariance matrix - from previously being diagonal to now turning non-diagonal.
5. The current OF being used is not equipped to handle this change.

---
Possible solutions
- Hybrid optimal filter- Computationally intensive
- Apply anti-aliasing before downsampling - Work ongoing
- Two-speed optimal filter

---
Two-speed optimal filter
- Adaptation of existing OF
- Handles correlations effectively
- Approach: Deals with slow and fast sampled regions separately and combines the results using appropriate covariance matrix.

---
Method
Take a hybrid trace
Extract fast region
Uniformly downsample signal
Apply OF
Amplitude, A2
Time delay, t0
Move template to right position using t0
Apply OF
Combine using Covariance matrix
Time delay=0
Amplitude, A1
COMBINED AMPLITUDE, A0

---
Finding the covariance matrix
1. Assume stationary noise.
2. Simulate 10,000 hybrid traces with same template and different noise generated from PD2 noise PSD.
3. Apply modified OF on all 10,000 traces.
4. Estimate covariance matrix between slow fit A1 and fast fit A2.
1. Blue: Generated PSD
2. Red: PD2 PSD

---
Importance of getting the time offset
The worse the time delay estimates are, the worse the amplitude estimates.

---
Shifting the template for slow fit
Time delay fits for delay drawn uniformly in the interval [-25.6,25.6]microsec.
Fits from full trace and fast region
Fits from uniformly downsampled trace

---
Combining the fit results
%chi^{ 2 }=left [ matrix{A_{1}-A_{0} #A_{2}-A_{0}} right ]*[covariance]^{ -1 }*left[matrix{ A_{1}-A_{0}## A_{2}-A_{0}} right]
Minimizing this:
A_{ 0 }= {(a+b)*A_{1}+(b+c)*A_{2}} over {a+2b+c}
where,
[covariance]^{-1}=left [ matrix{a # b ## b # c} right ]

---
Results
Errors on amplitude estimates:
- Fast region fit, A2 : 1.81-1.84%
- Uniformly downsampled fit, A1 : 1.9-1.94%
- Full trace fit, A32768 : 1.77-1.81%
- Combined fit, A0: 1.79-1.82%
  Combined fit result is nearly as good as the result from the full non-downsampled trace.

---
Future prospects
Implementing the two-speed NxM filter.