Two-speed Minimizer
By :
Aditi Pradeep
University of British Columbia

---
Hybrid readout scheme
Phonon trace
Charge trace

---
Correlation in hybrid readout
2. In the optimal filtering process, this results in a change in the covariance matrix - from previously being diagonal to now turning non-diagonal.
5. The current OF being used is not equipped to handle this change.

---
Possible solutions
- Hybrid optimal filter- Computationally intensive
- Apply anti-aliasing before downsampling - Work ongoing
- 2-speed optimal filter
- 2-speed minimizer

---
2-speed optimal filter
- Adaptation of existing OF
- Handles correlations effectively
- Approach: Deals with slow and fast sampled regions separately and combines the results using appropriate covariance matrix.

---
2-speed OF Results
Errors on amplitude estimates:
- Fast region fit, A2 : 1.81-1.84%
- Uniformly downsampled fit, A1 : 1.9-1.94%
- Full trace fit, A32768 : 1.77-1.81%
- Combined fit, A0: 1.79-1.82%
  Combined fit result is nearly as good as the result from the full non-downsampled trace.

---
Comments from the last meeting
- Dependance of the 2-speed OF on the covariance matrix is important.
- Need to test the dependance of the covariance matrix on pulse shape and look at how this affects the final result.
  SOLUTION: 2-speed minimizer

---
2-speed Minimizer
- Include pulse-shape parameters in the fit, for eg. fall time of the pulse.
- Inclusion of pulse-shape parameters is expected to account for the uncertainty arising from difference in pulse shapes.
- Perform the fit using Minuit.
- The result is now obtained from a simple 3 parameter fit (amplitude, time delay, fall time).
- The fit can be easily extended to include more parameters.

---
Method
Take a hybrid trace
Extract fast region
Uniformly downsample signal
A1
t1fall
t2fall
A2
t1d
t2d
Combine using 6x6 Covariance matrix
COMBINED AMPLITUDE, A0
COMBINED delay, t0d
COMBINED TFALL, t0fall
Minuit
Minuit

---
Combining the fit results
%chi^{ 2 }=left [ matrix{A_{1}-A_{0} #A_{2}-A_{0} #t^d_1-t^d_0 #t^d_2-t^d_0 #t^fall_1-t^fall_0 #t^fall_2-t^fall_0} right ]*[covariance]^{ -1 }*left[matrix{ A_{1}-A_{0}## A_{2}-A_{0} ## t^d_1-t^d_0 ##t^d_2-t^d_0 ##t^fall_1-t^fall_0 ##t^fall_2-t^fall_0} right]
Minimizing this chi square numerically returns the best fit parameters A0, t0d, t0fall.

---
Results

---
Results
Comparing the different fits obtained
Trace	Amplitude	Delay (std in us)	Fall Time
Fast sampled	1.82%	0.2235	3.23%
Uniformly downsampled	2%	0.58	4.41%
Best fit	1.799%	0.2233	3.20%

---
Results
Comparing different methods:
To compare different methods fall time was assumed to be known and delay was set to zero.
Method	Error on amplitude fit
OF	1.79%
HOF	3.06%
2-Speed OF	1.809%
2-Speed Minimizer	1.81%

---
Results
Comparing different methods:
The HOF was found to work just as well as the standard OF by Bill Page in his thesis. However, this analysis finds it to be a little worse than the standard OF. We suspect that this might be due to significant numerical errors arising from the matrix inversion step of the HOF or perhaps a previously unaccounted mistake in the HOF implementation. This needs further investigation.

---
Pros and cons
Pros
- Easily extended to more parameters
- Easy to adapt into an NxM version
- Reduced dependence on pulse shape
  Cons
- A little slower than 2-speed OF
- Occassional non-convergance (~2/3000), but these can easily be separated using a simple chi square cut.

---
Chi-square function
This method heavily relies on the chisq function and therefore, it is important that its dependance on the fit parameters are accurately represented.
Amplitude and pulse-shape parameter dependance is straight-forward.
Time delay is accounted through the phase term. We can construct this phase term in 2 ways:
1. Hard code the phase term into the chisq and then scan over a window, i.e. bin and then scan for the result.
2. Let the Fourier transform procedure convert the delay into a phase, i.e scan and then bin the result.

---
Chisq vs delay (in us)
No hard coded phase term in chisq function
Hard coding the phase term in chisq function
When the phase term is hard coded, it produces squiqqles which are artifacts of the binning. Binning after you fit is a more effective and faster technique.
The 2-Speed minimizer uses the second approach- by actually shifting the analytic template and rebinning it at each step of the fit, rather than by trying to "correct" the phase factors using the complex phase of the FFT coefficients.